## Slide 1: SONYC Assembly and Test

## Slide 2: Pre-assembly

## Slide 3: Test microphone function
Plug in mic to MCHStreamer and record snippet of audio on your machine. Play back to make sure recording is clear with no artifacts.

## Slide 4: Flash SD cards
Flash SD Cards and check it boots with SONYC code.
- download and install the necessary packages (ansible, hellolan, git clone ht.., ...)
- download rasbpi os
- repeat for all SD cards
- insert sd card
- run python setup_sd.py --vars "uuid=$(randomname get),app_name=sonyc"
- the first time you will be asked for wifi credentials, and next time it'll be cached
- record the uuid value printed out on masking tape
- Run ansible setup script
- go to overview.master1.sonycproject.com
- turn on "freshly provisioned" filter to
- check:
- tun0_ip: is openvpn up and running?
- wlan0_ip: is wifi working?
- ap: is the wifi ssid correct
- mic_connected:
- lzeq: is spl working

## Slide 5: Drill all Pi, Piwatcher, and LTE hat holes to fit 4-40 thru hole (use a 1/8” bit)
Clean with compressed air

## Slide 6: Assembly

## Slide 7: Place water membrane over microphone hole. Use 2 pairs of tweezers and place carefully to avoid touching adhesive. Press around the edge to adhere

## Slide 8: Screw in microphone PCBA

## Slide 9: Plug microphone cable into raspberry pi
Use jig to tell which pins to go into

## Slide 10: Plug antennas and LTE chip into cell hat

## Slide 11: Plug Piwatcher into the Pi Place a 7/16” spacer between the Piwatcher and Pi to support

## Slide 12: Place Cell Modem face up, with screws coming upwards through the holes. The long screw (1 1/8” long) goes on the bottom right corner (as shown).
Put 5/16” spacers on screws

## Slide 13: Put raspberry pi over screws on LTE hat (face up) and secure with o-rings ensure Piwatcher spacer catches long screw

## Slide 14: Connect LTE hat to Pi with right angle USB/Micro-usb cable. Plug it into the bottom right USB port (photo shows wrong one)

## Slide 15: Apply heat transfer paste to heatsink block

## Slide 16: Put back plate over PCB stack, flip, and screw PCBAs into PEMs on back plate (all PCBs face “down” towards back plate)

## Slide 17: Place rubber gasket over back plate assembly

## Slide 18: Adhere small gasket to front housing with double stick tape

## Slide 19: Attach antennae to housing as shown below
Main antenna is square-ish, goes on the back face (black wire). Route under white diversity antenna wire and secure cable to housing
Diversity antenna is long, goes on a side wall (can be bent to fit) (white wire)

## Slide 20: Twist mic cable wires, rout away from GPU and close to housing. Plug microphone cable into microphone PCBA

## Slide 21: Plug power cable into Pi. Install a zip-tie with a bit of slack internal to the housing.

## Slide 22: Electrical Inspection

## Slide 23: Test Cell shield, RPi, PiWatcher, SD Card
Use Balena Dashboard for node bringup. Dashboard will confirm success/failure.

## Slide 24: Close housing, keeping power cable between layers of silicone as shown. Screw to close with socket head screws, starting with the two on either side of the power cable.

## Slide 25: Pack into box with USB power adaptor, extension cord, and 2 large command strips.
Alternatively, would it be better if we shipped units just wrapped in bubble wrap? High volume when you put each one in a box.